## Slide 1
OPCON STREAM INs and OUTs
720p
RAW Video-01
[Network]
[Command-05]
1080p
Replay Video
[Local Disk]
[Command-04]
1080p
IP Camera-01
[Network]
[Command-03]
1080p
IP Camera-02
[Network]
[Command-03]
720p
RAW Video-02
[Network]
[Command-05]
UHD – HEVC Outbound Video Stream
[Command-01]
Stereo – AAC Outbound Sound Stream
[Command-02]
OPCON-01
[CENTOS 6.X]
[FFMPEG 3.4.1]
[NVENC 8.0.X]
[NO-CUDA]
[DRIVER 384.111]

## Slide 2
OPCON-02
[CENTOS 6.X]
[FFMPEG 3.4.1]
[NVENC 8.0.X]
[NO-CUDA]
[DRIVER 384.111]
UHD
Live Video Play
[Network]
[Command-07]
UHD
Live Video Record
[Network]
[Command-06]
OPCON – OPCON Live Play & Record
AAC - PULSE
Live Sound Play
[Network]
[Command-08]

## Slide 3
[Command-01] - Screen Stream – [OUT-bound]
ffmpeg -f x11grab -framerate 25 -video_size uhd2160 -i :0.0 -c:video hevc_nvenc -preset fast -pix_fmt bgr0 -b:v 3M -g 25 -an -f rtp_mpegts rtp://225.0.5.20:6000
[Command-02] - Line-In Stream - [OUT-bound]
ffmpeg -f alsa -i hw:0,0 -c:audio aac -b:a 36K -f rtp_mpegts rtp://225.0.5.20:6002
[Command-03] - 1080p Camera - [IN-bound]
ffmpeg -v debug -buffer_size 500000 -c:v h264_cuvid -i rtsp://10.0.5.249/video -pix_fmt yuv420p -f sdl "249"
ffmpeg -v debug -buffer_size 500000 -c:v h264_cuvid -i rtsp://10.0.5.250/video -pix_fmt yuv420p -f sdl "250"
[Command-04] - 720p recorded video
ffplay -v debug -vcodec hevc_cuvid Videos/the.expanse.s02e11.720p.hdtv.hevc.x265.rmteam.mkv
[Command-05] - 720p RAW Video - [IN-bound]
ffmpeg -v debug -re -probesize 32 -buffer_size 500000 -protocol_whitelist file,rtp,udp -strict -2 -i test.106.sdp -pix_fmt yuv420p -f sdl "106"
ffmpeg -v debug -re -probesize 32 -buffer_size 500000 -protocol_whitelist file,rtp,udp -strict -2 -i test.107.sdp -pix_fmt yuv420p -f sdl "107"
[Command-06] - OPCON Live Stream Remote Record - 20 minute - Owerwrite file - Copy Video Stream - No Audio Stream
ffmpeg -y -t 1200 -buffer_size 500000 -i rtp://225.0.5.20:6000 -vcodec copy -an opcon-10.mkv
[Command-07] - OPCON Live Stream Remote Play - [OPCON-OPCON] - [IN-bound]
ffmpeg -v debug -buffer_size 500000 -c:v hevc_cuvid -i rtp://225.0.5.20:6000 -pix_fmt yuv420p -window_fullscreen 1 -f sdl "opcon-10"
[Command-08] - OPCON Live Sound Stream Remote Play – [OPCON-OPCON] - [IN-bound]
ffmpeg -v debug -buffer_size 5000 -i rtp://225.0.5.20:6002 -buffer_size 5000 -f pulse default
SLIDE - 1/2 Commands

## Slide 4
OPCON – Advantech Live Play
UHD
Live Video Play
[Network]
[Command-09]
AAC - PULSE
Live Sound Play
[Network]
[Command-10]
LSDCU [ADVANTECH]
[CENTOS 7.X]
[VLC 3.0.X]
[FFMPEG 4.1]

## Slide 5
[Command-09] – LSDCU Live Video Stream Remote Play - OPCON-Advantech - [IN-bound]
ffmpeg -v debug -buffer_size 500000 -hwaccel vaapi -i rtp://225.0.5.20:6000 -pix_fmt yuv420p -window_fullscreen 1 -f sdl "opcon-10"
[Command-10] – LSDCU Live Sound Stream Remote Play - OPCON-Advantech - [IN-bound]
ffmpeg -v debug -buffer_size 5000 -i rtp://225.0.5.20:6002 -buffer_size 5000 -f pulse default
SLIDE – 4 Commands

## Slide 6
VIDEO
STREAMING SERVER
VIDEO
RECORDING SERVER
UHD
Live Video Record
[Network]
[Command-11]
UHD
Stream Recorded Video
[Network]
[Command-12]
EXTERNAL Live Record & Offline Stream

## Slide 7
[Command-11] – UHD Live Video Record
ffmpeg -y -buffer_size 500000 -thread_queue_size 256 -i rtp://225.0.5.20:6000 -buffer_size 5000 -thread_queue_size 256 -i rtp://225.0.5.20:6002 -map 0:0 -map 1:0 -c:v copy -c:a copy opcon-10.mkv
[Command-12] – UHD Stream Recorded Video
Work-In-Progress
SLIDE – 6 Commands

## Slide 8
OPCON
[CENTOS 6.X]
[FFMPEG 3.4.1]
[NVENC 8.0.X]
FFMPEG 3.4.1 – NVENC 8.0.X
Video Stream
25 FPS – 3 Mbit Bitrate
HEVC_NVENC – 25 GOP
RTP MPEGTS
YUV 420
FFMPEG 3.4.1- ALSA
Sound Stream
48000 Hz – 2 Channel
AAC – 36 Kbit
RTP MPEGTS
Video
Sound
LSDCU [ADVANTECH]
[CENTOS 7.X]
[VLC 3.0.X]
Video
Sound
FFMPEG 3.4.1 – NVENC 8.0.X
Video Stream
25 FPS – 3 Mbit Bitrate
HEVC_NVENC – 25 GOP
RTP MPEGTS
YUV 420
FFMPEG 3.4.1- ALSA
Sound Stream
48000 Hz – 2 Channel
AAC – 36 Kbit
RTP MPEGTS
VIDEO
RECORDING SERVER
VIDEO
STREAMING SERVER
FFMPEG
Compose Sound & Video
Record in MP4/MKV format
FFMPEG
Stream Sound & Video
RTP MPEGTS
Video
Sound
1080p
IP Camera
1080p
Replay Video
720p
RAW Video
1080p
IP Camera
720p
RAW Video
VIDEO Stream & Replay & Record